# Jakarta, 11 October 2013

# No. 1514/F30120/2013-S6

# Subject	: Invitation to bid, MR – CO

Dear Sir,

PT. PERTAMINA (PERSERO), Marketing & Trading Directorate – Shipping, hereby invites Shipowners/Brokers to bid for a trading vessel, with the following specification, term, and condition:

- Open Bid System

This bid shall be proceed by an open bid system, therefore we invite all reputable shipping company as owner or as broker/agent to participate in this bid without necessarily required to provide Pertamina Bid Registration (Surat Keterangan Terdaftar/SKT).

Detail terms and conditions of the bid procedure will be presented at the prebid meeting agenda with the schedule as mentioned in this invitation to bid.

- Technical Specifications MR – CO

| 1. | DWT / Hull | : | About | 35,000 MT | Double Hull |
| --- | --- | --- | --- | --- | --- |
| 2. | Year of Built & Flag | : | 1998 up | / | Indonesia / Foreign Flag |
| 3. | COT Capacity (98%) | : | Min. | 35,000 | M³ |
| 4. | Safe Draft | : | Max. | 12.5 | M |
| 5. | LOA | : | Max. | 190 | M |
| 6. | Service Speed | : | Min. | 12 | Knots |
| 7. | Type of Cargo | : | Crude / Black Oil Product, LSWR, HVGO, Decant Oil |
| 8. | Cargo Segregation | : | Min. | 3 | Grades |
| 9. | Cargo Heating | : | Maintain 140 Deg F / 60 Deg. C |
| 10. | Total Discharging Rate per Pump | : | Min. | 750 | M³/Hr/grade or 7 kg/cm² |
| 11. | Total Discharging Rate Cumulative | : | Min. | 1,200 | M³/Hr/grade or 7 kg/cm² |
| 12. | Total Loading Rate | : | Min. | 2,500 | M³/Hr |
| 13. | Cargo Pump | : | Min. | 2 | Unit |
| 14. | Bow Chain Stopper | : | Min. | 1 | Unit |
| 15. | Bottom Oil Sampler | : | Min. | 1 | Unit |
| 16. | Derrick / Crane | : | Min. | 10 | Ton |
| 17. | Segregated Ballast Tank | : | Required |
| 18. | Trading Area | : | Indonesia Waters |
| 19. | Vessel Tracking | : | Required Using Vessel Tracking Compatible With Pertamina’s Vessel Tracking |
| 20. | Lube Oil | : | Required Using Pertamina Product |
| 21. | Terminal Approval | : | Valid PSA (Pertamina Safety Approval) SIRE and KKKS Terminal Approval Minimum Pertamina Petrochina East Java (Tuban Marine Terminal), PHE WMO (Poleng Marine Terminal), Pertamina EP (Pangkalan Susu Terminal), Chevron, Conoco Phillips, pertamina ONWJ |

| 22. | Information | : | Internet on Board |
| --- | --- | --- | --- |
| 23. | Revetting applied every | : | 1 (one) year for vessel with YOB 0-5 years 6 (six) months for vessel with YOB above 5 years |

- Time Charter Term and Conditions

| 1. | Unit Vessel | : | 1 (one) Unit |
| --- | --- | --- | --- |
| 2. | Main Charter Periode | : | 3 | Months |
| 3. | Charterers Option Period | : | 1+1 | Month |
| 4. | Laycan | : | 25 – 30 October 2013 |
| 5. | Pertamina Safety Approval | : | Required |
| 6. | Charter Party | : | Pertatime III |

- Pertamina Safety Approval (PSA) Requirement

  - All vessels which will be offered in this bidding process are required to have Pertamina Safety Approval (PSA) issued by SMR Dept. Pertamina. This PSA shall be delivered along with the bid document at the bid closing time.

  - Any offering submitted without Pertamina Safety Approval (PSA) will be disqualified.

  - Referring to the above requirement, we recommend potential bidder to contact our SMR Dept for further detail regarding the Pertamina Safety Approval (PSA) procedure at the contact address below.

- Other Terms and Conditions & the Bid Schedule

- The Terms of Reference (ToR) shall be available to be downloaded at our website http://www.pertamina.com/ShippingProcurement.aspx.

- Bidding Schedule :

| AGENDA | DATE | TIME | TEMPAT |
| --- | --- | --- | --- |
| Pre Bid Meeting | 16 October 2013 | 10:00 | PT. PERTAMINA (PERSERO) Marketing & Trading Directorate – Shipping Jl. Yos Sudarso 32-34, Tg. Priok Jakarta 7th Floor Meeting Room |
| Bid Closing | 18 October 2013 | 10:00 |  |

Regards,

# Marketing & Trading Directorate – Shipping

Chartering Manager,

# I Putu Benedin

| CONTACT PERSON |
| --- |
| CHARTERING DEPT. | S M R DEPT. |
| Abdullah Faishol +62 21 430 1086 Ext 8343 +62 812 1090 138 (Mobile) abdullah.faishol@pertamina.com | Ade Aulia Safitri +62 21 430 1086 Ext 8430 +62 811 930 1912 (Mobile) ade.safitri@pertamina.com | Heinrich Parera +6221 4301086 Ext 8669 +62 81398884441 (Mobile) heinrich_parera@ pertaminashipping.com |