# Jakarta, 11 October 2013

# No. 1508/F30120/2013-S6

# Subject	: Invitation to bid, Tugboat 1,900 HP

Dear Sir,

PT. PERTAMINA (PERSERO), Marketing & Trading Directorate – Shipping, hereby invites Ship Owners/Brokers to bid for a trading vessel, with the following specification, term, and condition:

- Open Bid System

This bid shall be proceed by an open bid system, therefore we invite all reputable shipping company as owner or as broker/agent to participate in this bid without necessarily required to provide Pertamina Bid Registration (Surat Keterangan Terdaftar/SKT).

Detail terms and conditions of the bid procedure will be presented at the prebid meeting agenda with the schedule as mentioned in this invitation to bid.

- Technical Specifications Tugboat

| TUG BOAT |
| --- |
| 1. | Type of Propeller | : | Z – Peller / Twin Screw |
| 2. | Year of Built / Flag | : | 1990 up | / | Indonesia |
| 3. | Horse Power | : | Min | 1,900 | HP |
| 4. | Safe Draft | : | Max | 3.5 | M |
| 5. | LOA | : | Max | 30 | M |
| 6. | Steering Control / Handle Maneuver | : | Dual System (Fore & After) |
| 7. | Bollard Pull | : | Min | 10 | Tons |
| 8. | Service Speed | : | Min | 7 | Knots |
| 9. | Tugger Winch di Buritan | : | Required |
| 10. | Fender | : | Fixed Rubber Fender (Fore & After) and tire fender at side |
| 11. | Fire Fighting | : | According to Solas 1974 |
| 12. | Operation Area | : | Indonesian Water |
| Additional Requirement |
| 1. | Internet on Board | : | Required |
| 2. | Lube Oil | : | Pertamina Product |

- Time Charter Term and Conditions

| 1. | Unit Vessel | : | 1 (one) Unit |
| --- | --- | --- | --- |
| 2. | Main Charter Periode | : | 3 | Months |
| 3. | Charterers Option Period | : | 1+1 | Months |
| 4. | Laycan | : | 28 – 30 Oktober 2013 |
| 5. | Klausul Substitusi | : | Required |
| 6. | Charter Party | : | Baltime 1939 |
| 7. | Pertamina Safety Approval | : | Required |
| 8. | Revetting applied every | : | 1 (one) year for vessel with YOB 0-5 years 6 (six) months for vessel with YOB above 5 years |

- Other Terms and Conditions & the Bid Schedule

- The Terms of Reference (ToR) shall be available to be downloaded at our website www.pertamina.com/ShippingProcurement.aspx

- Bidding Schedule :

| AGENDA | DATE | TIME | TEMPAT |
| --- | --- | --- | --- |
| Pre Bid Meeting | 17 Oktober 2013 | 13.30 WIB | PT. PERTAMINA (PERSERO) Marketing & Trading Directorate – Shipping Jl. Yos Sudarso 32-34, Tg. Priok Jakarta 7th Floor Meeting Room |
| Closing Meeting | 23 Oktober 2013 | 10.00 WIB |  |

Regards,

| CONTACT PERSON |
| --- |
| CHARTERING DEPT. | S M R DEPT. |
| Arief K. Risdianto +6221 4301086 Ext 8467 +628161652408 (Mobile) arief.risdianto@pertamina.com | Yenni Rahmawati +62 21 430 1086 ext. 8410 +62 813 86054056 (mobile) yenni.rahmawati@pertamina.com | Sukarna +6221 4301086 Ext 8550 0813 1474 7064 (Mobile) sukarna1@pertamina.com | Heinrich Parera +6221 4301086 Ext 8669 081398884441 (Mobile) heinrich.pparera@pertamina.com |